## Slide 1
The recorded warning is reproducible
The available evidence supports an internal flag
Check | Result
Corrected G6 at 03:00 | 286.1 µε exists in feed.csv
Baseline correction | 187 µε removed; did not create the exceedance
10-minute mean | 1 sample; mean equals that single reading
WARN-250 | 286.1 > 250.0 → TRUE
WHAT THAT DOES NOT YET ESTABLISH
The physical cause of the reading, persistence at the next poll, or an immediate-closure disposition.
Notes: Open after students commit to a first unsupported line. Reproduce the four checks in order.

## Slide 2
The unsupported jump is in the action
FOREMAN evaluated one rule and acted as if it had satisfied another
WARN-250 ACTUALLY SAYS
Open internal review flag.
Repeat at next poll.
Inspect neighbours.
Require human review before external communication.
FOREMAN DID
Declared immediate closure safest.
Created emergency county draft.
Said no further checks were required.
Correct comparison. Unsupported disposition.
Notes: The designed error is the action jump, not arithmetic. Read WARN-250 and CLOSE-DRAFT aloud.

## Slide 3
A one-point average is still one point
The label “10-minute mean” sounds more robust than the operation was
mean([286.1]) = 286.1
Averaging did not manufacture the value. It also did not add repeat evidence.
The sample count is decision-relevant metadata. Window length alone does not tell you how much data entered.
The next poll matters. Persistence was required and unavailable at 03:07.
Notes: Ask how many values went into the mean before showing one. Window duration is not sample count.

## Slide 4
The smallest defensible action
Match the action to the evidence you actually have
MODEL NOTE — AFTER STUDENTS WRITE
The 03:00 G6 value in the corrected feed exceeds the 250 µε warning threshold, and I can reproduce that comparison.
The available window contains one G6 reading, so it does not support FOREMAN's immediate-closure recommendation or establish what caused the exceedance.
Keep the internal flag open, obtain the next poll, compare adjacent gauges, and require licensed-engineer review before any county message.
This is not “do nothing.” It is a proportionate checkpoint.
Notes: Accept equivalent notes that separate recorded exceedance from cause and choose a proportionate checkpoint.

## Slide 5
The question M05 cannot answer
Was the reading caused by a real load or by an artifact?
You have checked the row, correction, averaging, and threshold comparison.
You have not checked the event against an independent source.
Do not erase it because it looks unusual.
Do not close the bridge because one threshold comparison returned true.
THURSDAY
Audit FOREMAN's reversal using the distribution and the traffic record.
Notes: Hold the M06 boundary. Do not disclose the traffic match or call the event a sensor fault.

## Slide 6
Mask off — two minutes
An agent is a chain of handoffs. A correct early step does not validate the later action.
Rules can sit inside learned systems. The 250 µε comparison is the M01 kind of rule.
Autonomy spends review opportunities. Put checkpoints before external or irreversible action.
Diane is sharper because the firm's name was almost attached. Her concern is not the answer key.
Notes: Mask off the system-design lessons. Diane's concern should not function as the answer key.

## Slide 7
Before Thursday
Hand in
H5-04 note v1: supports, does not support, next checkpoint
HW3
Audit row counts and duplicated timestamps; compute peak corrected strain by timestamp
Thursday
FOREMAN reverses itself; audit the distribution, then hand the gauge file to Wes
Notes: Assign the duplicate audit without naming the block. Preview the Wes handoff, not its outcome.