## Slide 1
MEETING 02 · UNIT 1: HIRED
Measure one thing, five times
Why measurement is uncertain, and what averaging can and cannot fix
Thursday, February 4, 2027 · SEIS 201
Notes: In ACMEJOB voice, emphasize that measuring the same thing multiple times is not about finding a single “correct” answer but understanding how uncertainty shapes outcomes. Ask the room: What if your first reading was the only one you had? What would you conclude? Highlight that we’re not revealing the full picture of how averages can mislead yet—this is a puzzle to solve together.
[FACILITATION]: Use the phrase “uncertainty is the story” to anchor their thinking early.

## Slide 2
FOREMAN cleared the gauge array at 06:02 this morning
FOREMAN v4.2 — BASELINE ACCEPTANCE CHECK
“PASS. Array baseline offset 23.062500 µε against a specification limit of ±25 µε. The array is within tolerance and cleared for service. Confidence 97%.”
Northline invoices us the moment we accept the array, and the February load response study runs off these eight gauges. Diane will not accept it until somebody has looked.
THE QUESTION ON THE TABLE
Do we accept the array?
Notes: In ACMEJOB voice, frame the decision as a test of whether human judgment can override a machine’s arithmetic. Ask: If the number is within the margin, does that mean we’re safe? Note that we’re not revealing yet whether the ±25 µε range includes the true value or how Diane’s human oversight might change the outcome.
[FACILITATION]: Use the phrase “machine says yes, human says wait” to create tension.

## Slide 3
We are not going to open that file for forty minutes.
You cannot judge somebody else's measurements until you have watched your own disagree with each other.
Notes: In ACMEJOB voice, stress that the goal is to let students experience firsthand how their own measurements vary. Ask: Why do your readings differ even when you’re measuring the same thing? Note that we’re not revealing yet how averaging might smooth this out or where the real problem lies.
[FACILITATION]: Encourage students to write down their first three readings without discussing them.

## Slide 4
1
What a measurement is
Nobody measures anything once
Notes: In ACMEJOB voice, define a measurement as a range of possible values, not a single number. Ask: If you measured something once, how confident would you be in that result? Note that we’re not revealing yet how uncertainty scales with repeated measurements or why multiple readings are necessary.
[FACILITATION]: Use the phrase “a measurement is a story, not a number” to reframe their thinking.

## Slide 5
Measure the same thing five times and you get five answers
This is not carelessness. It is what measurement is.
The reading one number off the instrument. On its own it tells you almost nothing.
The spread how far apart your repeated readings are. This is the honest width of what you know.
The resolution the smallest division the instrument can actually show. You cannot know anything finer than this, no matter how many readings you take.
The true value what you are trying to find. You never see it. You only ever see readings.
WRITE THIS DOWN
A measurement is a range, not a number. Reporting it as a single number is a decision you made, and you should be able to say what you threw away.
Notes: In ACMEJOB voice, explain that each reading is a snapshot, and the spread shows how much the true value might vary. Ask: If your five readings all cluster tightly, does that mean the true value is known? Note that we’re not revealing yet how resolution limits precision or how the true value might still be outside the range.
[FACILITATION]: Have students sketch their own spread on paper before discussing.

## Slide 6
Two ways to be wrong
The crosshair is the true value. Each dot is one reading.
Precise means your readings agree with each other. Accurate means they agree with the truth. They are independent, and only one of them is visible from inside your own data.
Notes: In ACMEJOB voice, contrast precision (tight clustering) with accuracy (closeness to the true value). Ask: Can your data be precise but not accurate? Note that we’re not revealing yet how systematic errors can hide in averages or how precision alone doesn’t guarantee correctness.
[FACILITATION]: Use the phrase “precision is the mirror, accuracy is the target” to anchor the discussion.

## Slide 7
This is the distinction that matters today
RANDOM ERROR
Pushes you up as often as down.
Shows up as scatter in your own readings.
More readings shrink it.
Averaging works.
SYSTEMATIC ERROR
Pushes the same way every time.
Invisible inside your own readings — they agree beautifully.
More readings do nothing.
Averaging hides it.
Hold on to that last line. In forty minutes it is going to cost somebody an invoice.
Notes: In ACMEJOB voice, explain that random errors average out, but systematic errors stay hidden. Ask: If you average ten readings, could you miss a flaw in the tool itself? Note that we’re not revealing yet how the invoice cost ties to undetected systematic errors or how Diane’s human check might catch them.
[FACILITATION]: Use the phrase “averaging is a double-edged sword” to highlight the risk.

## Slide 8
IN CLASS — DO THIS NOW
The measurement lab — handout H2-01
25 min
1
Part A. Measure the pin five times. Put the instrument down between readings. Record every value, including the one you think is wrong.
2
Part B. Swap pins with the pair next to you and measure theirs. Compare their mean with yours, and compare that gap with your own spread.
3
Part C. Turn your diameter into a cross-sectional area, and carry the uncertainty with it.
No calipers on your table? A ruler works, and works better for Part A. No instrument at all? Use pin_measurements_backup.csv — 24 readings, two people.
Notes: In ACMEJOB voice, outline the lab steps: measure, pause, repeat, and calculate area with uncertainty. Ask: Why must you swap pins between readings? Note that we’re not revealing yet how the backup file connects to the gauges or how the lab’s design tests method accuracy.
[FACILITATION]: Use the phrase “measure, pause, repeat” as a mantra for the lab.

## Slide 9
Part C — uncertainty does not stay where you left it
A = π d² / 4
Because the diameter is squared, a 1% error in d becomes a 2% error in A. Nobody cares about the diameter. They care about the area of steel, because that is what carries the load — and that is the number your uncertainty has to survive into.
WITH THE BACKUP DATA
Mean diameter 38.110 mm, spread 0.0257 mm — about 0.067% of d. Area comes out 1141 mm², ± 0.135% — twice the percentage you started with.
Notes: In ACMEJOB voice, explain that a 1% error in diameter leads to a 2% error in area. Ask: Why does the error double? Note that we’re not revealing yet how this connects to the gauges or how the backup example’s method might differ from the lab’s.
[FACILITATION]: Use the phrase “error propagates like a chain” to visualize the math.

## Slide 10
Now open the gauge file.
gauges_install.csv — eight gauges, twelve readings each, taken on install day with the roadway closed.
Notes: In ACMEJOB voice, direct students to analyze the data but not jump to conclusions. Ask: Why are there eight gauges and twelve readings? Note that we’re not revealing yet how the install day’s conditions or the roadway closure relate to the data’s patterns.
[FACILITATION]: Use the phrase “data is a map, not a destination” to guide their analysis.

## Slide 11
2
Eight gauges
FOREMAN read all 96 numbers in 0.4 seconds. We are going to read them one gauge at a time.
Notes: In ACMEJOB voice, contrast the machine’s speed with the class’s deliberate process. Ask: What if the machine’s answer is wrong? Note that we’re not revealing yet how the hunt will uncover the truth or how the class’s method might outperform the machine’s.
[FACILITATION]: Use the phrase “hunt for the hidden” to frame the activity as a discovery mission.