## Slide 1
MEETING 06 · INSTRUCTOR REVEAL
What the records support.
Open only after students submit the audit decision
M06 · Unit 1 close
Notes: SAY: “Now we compare what the evidence supports. This is the reveal, not a reward for choosing Diane's preference.”

## Slide 2
The selected daily peaks are strongly right-tailed
15 days · median 110.7 µε · range 104.0–286.1 µε
WHAT THE HISTOGRAM SHOWS
Most daily peaks cluster near 104–121 µε.
One extreme event extends the right tail.
The small set of selected maxima does not justify FOREMAN's normal model.
WHAT IT DOES NOT SHOW
The physical cause
Whether the bridge was unsafe
Whether the sensor failed
Notes: SAY: “The shape is right-tailed, and there are only 15 selected maxima. FOREMAN's normal assumption is not earned.”

## Slide 3
The duplicate block is real—and irrelevant to 03:00
February 12, 14:00–15:00 ≠ February 16, 03:00
PIPELINE AUDIT
The duplicate payload changes row counts. It does not create, repeat, or alter the alarm event or its daily peak.
LESSON
Finding one pipeline defect does not license deleting a different unusual value.
Notes: SAY: “The duplicated timestamps matter for later analyses, but they occur on another day. A real defect is not a universal explanation.”

## Slide 4
The independent record aligns at 03:00
Kinnick County bridge traffic counter
Timestamp | Direction | Class | Axles | Estimated gross weight
2027-02-16 03:00 | EB | 5-axle heavy vehicle | 5 | 79,400 lb
BOUNDARY
Timestamp alignment and the cross-gauge response support retaining the event. They do not alone establish safety or prove a load-response mechanism.
Notes: SAY: “The traffic counter aligns with the gauge event. That is independent corroboration, not a complete safety analysis.”

## Slide 5
Tuesday overreacted. Thursday overcorrected.
A real event still needs a bounded engineering disposition.
Notes: SAY: “Tuesday, FOREMAN jumped from warning to closure. Thursday, it jumped from unusual to fault. Both skipped evidence.”

## Slide 6
A defensible record keeps the event and its limits
MODEL DECISION — NOT THE ONLY FULL-CREDIT WORDING
“I retained and annotated the 03:00 reading because it appears in the corrected feed, all gauges rise at the same timestamp, and the traffic counter records a heavy vehicle then. The duplicate block occurs on a different day. This supports a real event, not by itself a safety disposition; next I would verify the vehicle estimate and bridge response.”
Notes: SAY: “Full credit follows the trace and limits. Retain or quarantine can be defensible; unsupported deletion cannot.”

## Slide 7
Unit 1 · mask off
Compare verification choices, not character approval
M01 A traceable rule and a learned pattern answer different questions.
M02 Averages can hide measurement problems.
M03 Fluent citations still require the source.
M04 A mean can hide the spread.
M05–M06 Audit every agent handoff; unusual is not the same as wrong.
Notes: SAY: “Mask off. Which check changed your wording? Which did you not buy with your project hours?”

## Slide 8
The file leaves their desk
LOG
Collect the decision and what remained unchecked.
COVER
Students complete H6-04 and the workbook Wes handoff sheet.
HAND OFF
Each student gives the February gauge workbook to Wes.
INSTRUCTOR
Preserve the submitted file unchanged. Do not announce its later return.
Notes: SAY: “Complete the handoff now. The receiving engineer needs the unchecked items as much as the chart.” Preserve student files; do not mention M25.