## Slide 1
MEETING 13 · INSTRUCTOR REVEAL
Silent ingestion
Open only after students commit one end-to-end trace
M13 · Unit 2: Doubt
Notes: M13 CANON SAY — Cloud hard-review PASS.
REVEAL — Open only after students commit H13-01. SAY: “FOREMAN’s designed error is silent ingestion. It never stops to ask.”

## Slide 2
FOREMAN never stopped to ask.
A COMPLETE run can preserve every hidden assumption.
Notes: M13 CANON SAY — Cloud hard-review PASS.
REVEAL — SAY: “A complete run is not an honest run. The status only says that the configured steps executed.”

## Slide 3
The row count changes without an exception record
SOURCE
12 sensor records
10 weather records
EMITTED
10 joined model records
Status: COMPLETE
No operator question
Notes: M13 CANON SAY — Cloud hard-review PASS.
REVEAL — SAY: “Twelve sensor records entered, ten weather records existed, and ten model records emerged. The inner join removed unmatched source records without an exception record.”

## Slide 4
One field carries more than one unit
SOURCE COLUMN
lateral_offset includes feet and millimetres
Worked record: OB-103 = 130 mm
INGESTION DEFAULT
Numeric token extracted
Every value assigned schema_unit = ft
No unit exception generated
Notes: M13 CANON SAY — Cloud hard-review PASS.
REVEAL — SAY: “The source field mixes feet and millimetres. FOREMAN extracts the numeric token and applies a default-foot schema to every row.”

## Slide 5
Worked trace · OB-103
FOREMAN PATH
Offset = 130.000 ft
Alignment adjustment = 1040.00 µε
Model input = 1163.42 µε
UNIT-AWARE PATH
Offset = 0.4265 ft
Alignment adjustment = 3.41 µε
Model input = 126.83 µε
Notes: M13 CANON SAY — Cloud hard-review PASS.
REVEAL — SAY: “For OB-103, FOREMAN treats 130 mm as 130.000 feet. The unit-aware path converts it to 0.4265 feet. The difference grows in the adjustment and reaches the downstream model input.”

## Slide 6
The human and machine failures rhyme
WES’S HANDOFF
Late
Two promised sheets absent
Assumptions undocumented
FOREMAN’S INGESTION
Defaults replace questions
Rows disappear quietly
Run status says COMPLETE
Notes: M13 CANON SAY — Cloud hard-review PASS.
REVEAL — SAY: “Wes’s thin handoff and FOREMAN’s silent ingestion share one failure mode: undocumented assumptions continue downstream. Keep the M07 memo/bearing-wear item as liability color only.”

## Slide 7
A bounded review record is the deliverable
MODEL NOTE v2 · NOT REQUIRED WORDING
I traced OB-103 through source, parse, join, adjustments, and output.
The path should stop at ingestion because source records disappear without an exception record and a mixed-unit value is processed under one default unit.
I did not review every field; the unchecked fields are logged separately.
Notes: M13 CANON SAY — Cloud hard-review PASS.
NOTE — SAY: “A complete audit is not required. An honest trace plus an unchecked-column log is required. Grade the record, not agreement with Diane’s schedule pressure.”

## Slide 8
Close Unit 2 without erasing the record
REVEAL
Silent ingestion: FOREMAN never stops to ask.
DEBRIEF
Run the full 15-minute mask-off beat after Note.
STORY
M07 liability color stays in the inbox; Wes does not co-solve.
SPOILER GUARD
Do not introduce any M14 overweight-permit details.
Notes: M13 CANON SAY — Cloud hard-review PASS.
CLOSE — SAY: “After this reveal, run the separate Unit 2 debrief. Do not preview the M14 exam scenario. Close on ownership: handoff, ship pressure, and review record.”