## Slide 1
EXAM 1 · LATER REVIEW ONLY
The record changes the call
Never open on exam day · use only after release is approved
M14 · Instructor review · Unit 2
Notes: M14 CANON SAY — Cloud PASS.
Clock lock: 75 writing minutes per the syllabus. Setup and collection are proctor overhead and are not subtracted from student writing time.
LATER REVIEW ONLY — Do not open on exam day. Use only in a separately scheduled review after exam materials are secured and release is approved.

## Slide 2
FOREMAN checked a number. You checked the basis.
Source · spread · interval · visual · scope
Notes: M14 CANON SAY — Cloud PASS.
Clock lock: 75 writing minutes per the syllabus. Setup and collection are proctor overhead and are not subtracted from student writing time.
REVIEW — SAY: “FOREMAN checked a number. Your exam record checked the source, spread, interval, visual, and scope.” Do not frame this as one correct decision reveal.

## Slide 3
Source check · the ratio is 1.30
FOREMAN states 25% and calculates with 1.25
SOURCE VALUES
Requested load = 104 kip
Test load = 80 kip
CHECK
104 / 80 = 1.30
Requested load is 30% above the test load
Notes: M14 CANON SAY — Cloud PASS.
Clock lock: 75 writing minutes per the syllabus. Setup and collection are proctor overhead and are not subtracted from student writing time.
SOURCE CHECK — Invite valid source checks before showing the ratio. The permit request gives 104 kip and the test record gives 80 kip; 104 / 80 = 1.30.

## Slide 4
Test data · center needs spread
CENTER
Mean = 173.6 µε
SPREAD
Sample SD = 11.6 µε
Range = 34.0 µε
SCOPE
8 repeated passes
One control gauge
One test condition
Notes: M14 CANON SAY — Cloud PASS.
Clock lock: 75 writing minutes per the syllabus. Setup and collection are proctor overhead and are not subtracted from student writing time.
SPREAD — Preserve supported rounding and units. Mean alone is not enough; the record needs spread and the one-gauge / one-condition scope.

## Slide 5
Scaled interval · close to the trigger
TEST-LOAD 95% INTERVAL
163.9 to 183.3 µε
Mean = 173.6 µε
PERMIT-LOAD SCREEN
Ratio = 1.30
Scaled interval = 213.1 to 238.3 µε
Instructional trigger = 240 µε
Notes: M14 CANON SAY — Cloud PASS.
Clock lock: 75 writing minutes per the syllabus. Setup and collection are proctor overhead and are not subtracted from student writing time.
INTERVAL — Walk the supplied t interval and ratio. State that direct load scaling is an exam simplification, not a real bridge rating method.

## Slide 6
The chart hides what the decision needs
VISUAL FRAMING
Axis starts at 200 µε
Small margin looks decisive
MISSING EVIDENCE
Only the average appears
No interval
No one-gauge scope
Notes: M14 CANON SAY — Cloud PASS.
Clock lock: 75 writing minutes per the syllabus. Setup and collection are proctor overhead and are not subtracted from student writing time.
CHART — Accept any consequential flaw grounded in the supplied chart. Do not require one phrase when the student explains why the flaw matters to a county reader.

## Slide 7
More than one call can be defensible
YES WITH CONDITIONS
Upper bound remains just below the classroom trigger
Retain speed, lane, one-crossing, review / monitoring conditions
NO / HOLD
Linear scaling is assumed
Margin is narrow
One gauge does not establish bridge-wide capacity
Notes: M14 CANON SAY — Cloud PASS.
Clock lock: 75 writing minutes per the syllabus. Setup and collection are proctor overhead and are not subtracted from student writing time.
DECISION — Do not crown one branch. YES WITH CONDITIONS and NO / HOLD are both defensible when the record is honest; unconditioned YES is usually weak.

## Slide 8
Unit 2 closes on a documented judgment
GRADE
Reasoning, traceability, uncertainty, assumptions, and scope.
DO NOT GRADE
Agreement with FOREMAN, Diane, or one preferred final outcome.
BOUNDARY
No later-unit methods, callbacks, or Otter Bend outcomes in this reveal.
CANON
Cloud-PASS SAY is folded; this deck is reserved for a separate later review.
Notes: M14 CANON SAY — Cloud PASS.
Clock lock: 75 writing minutes per the syllabus. Setup and collection are proctor overhead and are not subtracted from student writing time.
CLOSE — Score the reasoning and record. No M13 answers as free points, no Unit 3 content, and no later Otter Bend outcomes.