## Slide 1
MEETING 14 · INSTRUCTOR REVEAL
The record changes the call
Open only after every exam is collected
M14 · Exam 1 · Unit 2 close
Notes: M14 SAY HOLD — PLACEHOLDER ONLY — NOT CLOUD-PASS.
Do not deliver this text as canon. Replace only from the attached Cloud-PASS file in a follow-up.
RUN-OF-DAY HOOK: [POST-COLLECTION opening placeholder. Confirm all exam materials are secured before reveal.]

## Slide 2
FOREMAN checked a number. You checked the basis.
Source · spread · interval · visual · scope
Notes: M14 SAY HOLD — PLACEHOLDER ONLY — NOT CLOUD-PASS.
Do not deliver this text as canon. Replace only from the attached Cloud-PASS file in a follow-up.
RUN-OF-DAY HOOK: [REVEAL thesis placeholder. Distinguish a completed machine calculation from an engineering record.]

## Slide 3
Source check · the ratio is 1.30
FOREMAN states 25% and calculates with 1.25
SOURCE VALUES
Requested load = 104 kip
Test load = 80 kip
CHECK
104 / 80 = 1.30
Requested load is 30% above the test load
Notes: M14 SAY HOLD — PLACEHOLDER ONLY — NOT CLOUD-PASS.
Do not deliver this text as canon. Replace only from the attached Cloud-PASS file in a follow-up.
RUN-OF-DAY HOOK: [SOURCE-check walkthrough placeholder. Invite multiple valid source checks before showing the 1.30 ratio.]

## Slide 4
Test data · center needs spread
CENTER
Mean = 173.6 µε
SPREAD
Sample SD = 11.6 µε
Range = 34.0 µε
SCOPE
8 repeated passes
One control gauge
One test condition
Notes: M14 SAY HOLD — PLACEHOLDER ONLY — NOT CLOUD-PASS.
Do not deliver this text as canon. Replace only from the attached Cloud-PASS file in a follow-up.
RUN-OF-DAY HOOK: [DESCRIPTIVE-statistics placeholder. Preserve supported rounding and units.]

## Slide 5
Scaled interval · close to the trigger
TEST-LOAD 95% INTERVAL
163.9 to 183.3 µε
Mean = 173.6 µε
PERMIT-LOAD SCREEN
Ratio = 1.30
Scaled interval = 213.1 to 238.3 µε
Instructional trigger = 240 µε
Notes: M14 SAY HOLD — PLACEHOLDER ONLY — NOT CLOUD-PASS.
Do not deliver this text as canon. Replace only from the attached Cloud-PASS file in a follow-up.
RUN-OF-DAY HOOK: [INTERVAL walkthrough placeholder. State direct scaling as an exam simplification, not a real rating method.]

## Slide 6
The chart hides what the decision needs
VISUAL FRAMING
Axis starts at 200 µε
Small margin looks decisive
MISSING EVIDENCE
Only the average appears
No interval
No one-gauge scope
Notes: M14 SAY HOLD — PLACEHOLDER ONLY — NOT CLOUD-PASS.
Do not deliver this text as canon. Replace only from the attached Cloud-PASS file in a follow-up.
RUN-OF-DAY HOOK: [CHART critique placeholder. Accept other consequential critiques grounded in the supplied visual.]

## Slide 7
More than one call can be defensible
YES WITH CONDITIONS
Upper bound remains just below the classroom trigger
Retain speed, lane, one-crossing, review / monitoring conditions
NO / HOLD
Linear scaling is assumed
Margin is narrow
One gauge does not establish bridge-wide capacity
Notes: M14 SAY HOLD — PLACEHOLDER ONLY — NOT CLOUD-PASS.
Do not deliver this text as canon. Replace only from the attached Cloud-PASS file in a follow-up.
RUN-OF-DAY HOOK: [DECISION comparison placeholder. Keep YES WITH CONDITIONS and NO / HOLD both gradeable.]

## Slide 8
Unit 2 closes on a documented judgment
GRADE
Reasoning, traceability, uncertainty, assumptions, and scope.
DO NOT GRADE
Agreement with FOREMAN, Diane, or one preferred final outcome.
BOUNDARY
No later-unit methods, callbacks, or Otter Bend outcomes in this reveal.
SAY HOLD
Speaker language remains empty until a Cloud-PASS file is attached.
Notes: M14 SAY HOLD — PLACEHOLDER ONLY — NOT CLOUD-PASS.
Do not deliver this text as canon. Replace only from the attached Cloud-PASS file in a follow-up.
RUN-OF-DAY HOOK: [UNIT 2 close placeholder. No later-semester spoilers. Restate that Diane is not the grading key.]