## Slide 1
MEETING 08 · UNIT 2: DOUBT
A strong fit can still mislead.
Correlation, regression, mechanism, and a temperature confound
Thursday, February 25, 2027 · SEIS 201
Notes: OLI STORY/SAY STATUS: PENDING CLOUD PASS — DO NOT TREAT THIS HOOK AS CANON SAY.
PASTE APPROVED SAY HERE, preserving the instructional action below.
TITLE HOOK — Introduce M08 and Unit 2's next designed error. Preserve the distinction between a strong relationship and damage evidence.

## Slide 2
The interim finding
FOREMAN modeled G4 strain against date
FOREMAN · FINAL OUTPUT
Midspan strain rises with date. R² = 0.87.
Conclusion entered in the draft: progressive structural deterioration.
DECISION
Does this relationship support a damage claim—or is date standing in for something else?
Notes: OLI STORY/SAY STATUS: PENDING CLOUD PASS — DO NOT TREAT THIS HOOK AS CANON SAY.
PASTE APPROVED SAY HERE, preserving the instructional action below.
INBOX HOOK — Deliver the approved FOREMAN/Diane/Wes story beat here. Preserve: date-model R², deterioration overclaim, Diane in believer mode. Do not add later bearing-wear or exam details.

## Slide 3
The hunt
Reproduce · compare · explain · correct
1 REPRODUCE
Plot strain against date
Fit the reported line
2 COMPARE
Join weather
Plot strain against temperature
3 EXPLAIN
Name a physical mechanism
Set the causal boundary
4 CORRECT
Remove temperature-linked strain
Retest the date trend
Notes: OLI STORY/SAY STATUS: PENDING CLOUD PASS — DO NOT TREAT THIS HOOK AS CANON SAY.
PASTE APPROVED SAY HERE, preserving the instructional action below.
HUNT HOOK — Frame the four student actions without disclosing temperature as the answer before the hunt begins.

## Slide 4
1
See the relationship
A scatter plot comes before a coefficient
Notes: OLI STORY/SAY STATUS: PENDING CLOUD PASS — DO NOT TREAT THIS HOOK AS CANON SAY.
PASTE APPROVED SAY HERE, preserving the instructional action below.
TEACH TRANSITION HOOK — Move from story evidence into scatter plots.

## Slide 5
A scatter plot shows paired observations
Direction positive, negative, or no clear linear pattern.
Form linear, curved, clustered, or changing spread.
Strength how tightly points follow the pattern.
Exceptions outliers, gaps, or groups that need explanation.
FIRST MOVE
Plot before interpreting a fitted statistic.
Notes: OLI STORY/SAY STATUS: PENDING CLOUD PASS — DO NOT TREAT THIS HOOK AS CANON SAY.
PASTE APPROVED SAY HERE, preserving the instructional action below.
TEACH HOOK — Ask students what they inspect before calculating a coefficient.

## Slide 6
Correlation measures linear association
It does not identify the mechanism
CORRELATION COEFFICIENT r
Ranges from −1 to +1
Sign gives direction
Magnitude gives linear strength
NOT INCLUDED
Proof of cause
Protection from a hidden variable
Engineering significance
Notes: OLI STORY/SAY STATUS: PENDING CLOUD PASS — DO NOT TREAT THIS HOOK AS CANON SAY.
PASTE APPROVED SAY HERE, preserving the instructional action below.
TEACH HOOK — Define correlation coefficient and explicitly separate association from mechanism.

## Slide 7
Linear regression fits a prediction line
MODEL
response = intercept + slope × predictor
Slope: expected response change per predictor unit
CHECK
Units
Range represented
Residual pattern
Variables omitted
Notes: OLI STORY/SAY STATUS: PENDING CLOUD PASS — DO NOT TREAT THIS HOOK AS CANON SAY.
PASTE APPROVED SAY HERE, preserving the instructional action below.
TEACH HOOK — Connect slope units to an engineering interpretation.

## Slide 8
R² describes fit—not cause
R² CAN SAY
How much response variation is described by this fitted model in this sample
R² CANNOT SAY
The predictor caused the response
The model is complete
Damage is progressing
Notes: OLI STORY/SAY STATUS: PENDING CLOUD PASS — DO NOT TREAT THIS HOOK AS CANON SAY.
PASTE APPROVED SAY HERE, preserving the instructional action below.
TEACH HOOK — State that R² is fit in a sample, not a causation score.

## Slide 9
A model can fit the observed points and still tell the wrong story.
The causal claim needs a mechanism and competing explanations.
Notes: OLI STORY/SAY STATUS: PENDING CLOUD PASS — DO NOT TREAT THIS HOOK AS CANON SAY.
PASTE APPROVED SAY HERE, preserving the instructional action below.
TEACH HOOK — Invite an example of a fitted line that could still tell the wrong story.

## Slide 10
Spurious does not mean imaginary
REAL ASSOCIATION
Date and strain can move together
The fitted line can be computed correctly
MISLEADING CLAIM
Date may proxy another variable
The association does not establish deterioration
Notes: OLI STORY/SAY STATUS: PENDING CLOUD PASS — DO NOT TREAT THIS HOOK AS CANON SAY.
PASTE APPROVED SAY HERE, preserving the instructional action below.
TEACH HOOK — Define spurious correlation as a misleading inference, not fabricated data.

## Slide 11
2
Hunt the confound
Use the weather record, then name the mechanism
Notes: OLI STORY/SAY STATUS: PENDING CLOUD PASS — DO NOT TREAT THIS HOOK AS CANON SAY.
PASTE APPROVED SAY HERE, preserving the instructional action below.
LAB TRANSITION HOOK — Open the investigation without naming the temperature mechanism.

## Slide 12
IN CLASS — DO THIS NOW
Reproduce FOREMAN's model
8 min
1
Open feed.csv and plot corrected strain against date_index.
2
Fit a linear trendline; record slope and R² in H8-02.
3
Write one sentence the model supports without using a causal verb.
A reproduced statistic can still support an overclaimed interpretation.
Notes: OLI STORY/SAY STATUS: PENDING CLOUD PASS — DO NOT TREAT THIS HOOK AS CANON SAY.
PASTE APPROVED SAY HERE, preserving the instructional action below.
LAB A HOOK — Students reproduce FOREMAN's date model and write a noncausal description.

## Slide 13
IN CLASS — DO THIS NOW
Join the weather record
10 min
1
Use timestamp_cst to join feed.csv and weather_station.csv.
2
Check row counts, unmatched timestamps, duplicates, and °C units.
3
Plot strain against air_temperature_c; fit the second line.
4
Compare direction, slope units, and R² with the date model.
A clean join is part of the evidence, not clerical overhead.
Notes: OLI STORY/SAY STATUS: PENDING CLOUD PASS — DO NOT TREAT THIS HOOK AS CANON SAY.
PASTE APPROVED SAY HERE, preserving the instructional action below.
LAB B HOOK — Release weather_station.csv. Require timestamp and unit checks before modeling.

## Slide 14
IN CLASS — DO THIS NOW
Name the mechanism; set the boundary
8 min
1
Explain what warming does to steel and a restrained sensor location.
2
Draw date → temperature → measured strain on H8-03.
3
State why the date fit alone cannot distinguish thermal response from damage.
4
List evidence still needed before claiming structural deterioration.
A second correlation becomes useful when it has a plausible physical mechanism.
Notes: OLI STORY/SAY STATUS: PENDING CLOUD PASS — DO NOT TREAT THIS HOOK AS CANON SAY.
PASTE APPROVED SAY HERE, preserving the instructional action below.
LAB C HOOK — After students see the temperature relationship, elicit the thermal expansion mechanism.

## Slide 15
IN CLASS — DO THIS NOW
Set up the correction
4 min
1
Use the temperature model to calculate predicted strain.
2
Residual = observed strain − predicted temperature-linked strain.
3
Plot the residual against date and identify the claim that test can support.
Complete the full calculation in HW4; do not claim that one correction proves no damage.
Notes: OLI STORY/SAY STATUS: PENDING CLOUD PASS — DO NOT TREAT THIS HOOK AS CANON SAY.
PASTE APPROVED SAY HERE, preserving the instructional action below.
LAB D HOOK — Set up residual correction as HW4's method; preserve the distinction between 'not evidence of damage' and 'proof of no damage.'

## Slide 16
Write Unit 2 Note v2
Claim · check · result
CLAIM
State FOREMAN's exact deterioration inference.
CHECK
Name the weather join, model comparison, and mechanism.
RESULT
Bound what the uncorrected trend can support.
Notes: OLI STORY/SAY STATUS: PENDING CLOUD PASS — DO NOT TREAT THIS HOOK AS CANON SAY.
PASTE APPROVED SAY HERE, preserving the instructional action below.
NOTE HOOK — Students commit claim/check/result before the reveal.

## Slide 17
Before the gated reveal
HAND IN
H8-02 regression hunt and H8-05 Note version 2.
ASSIGNED
HW4: temperature-corrected strain trend.
RECORD
Project-hour choice and anything accepted unverified.
BOUNDARY
This meeting tests the trend claim; it does not settle bridge condition.
Notes: OLI STORY/SAY STATUS: PENDING CLOUD PASS — DO NOT TREAT THIS HOOK AS CANON SAY.
PASTE APPROVED SAY HERE, preserving the instructional action below.
CLOSE HOOK — Assign HW4 here. Insert approved story close when available; do not preview later Unit 2 revelations.