## Slide 1
MEETING 10 · UNIT 2: DOUBT
Did the deck get worse?
Separate a small paired signal from measurement and process noise
Thursday, March 4, 2027 · SEIS 201
Notes: OLI SAY PLACEHOLDER — CLOUD PASS PENDING.
Beat: title and meeting frame
Do not improvise or treat this scaffold as approved canon. Replace only from the Cloud-PASS M10 SAY file on follow-up.

## Slide 2
The yes-or-no request
FOREMAN has already made the answer sound final
FOREMAN · FINAL OUTPUT
Mean test-truck strain is up 6%. Deterioration confirmed.
p = 0.04, so there is a 96% chance the deck has deteriorated.
DIANE HALVORSEN, PE
Did the deck get worse since 2019—yes or no?
Notes: OLI SAY PLACEHOLDER — CLOUD PASS PENDING.
Beat: inbox: Diane, FOREMAN, and schedule pressure
Do not improvise or treat this scaffold as approved canon. Replace only from the Cloud-PASS M10 SAY file on follow-up.

## Slide 3
The hunt
Estimate · audit noise · change confidence · bound the claim
1 PAIR
Same eight locations
2027 minus 2019
2 QUANTIFY
Mean change
Standard error
3 AUDIT
Repeatability
Matched process controls
4 BOUND
95% versus 99%
Signal without overclaim
Notes: OLI SAY PLACEHOLDER — CLOUD PASS PENDING.
Beat: student hunt
Do not improvise or treat this scaffold as approved canon. Replace only from the Cloud-PASS M10 SAY file on follow-up.

## Slide 4
1
Build an interval
Start with six coupons; then move to eight paired changes
Notes: OLI SAY PLACEHOLDER — CLOUD PASS PENDING.
Beat: teach transition
Do not improvise or treat this scaffold as approved canon. Replace only from the Cloud-PASS M10 SAY file on follow-up.

## Slide 5
Standard error is uncertainty in the sample mean
SPREAD OF VALUES
Standard deviation describes variation among observations
The paired changes differ by location
SPREAD OF AN ESTIMATE
Standard error = s / √n
It estimates sample-to-sample variation of the mean
Notes: OLI SAY PLACEHOLDER — CLOUD PASS PENDING.
Beat: standard error
Do not improvise or treat this scaffold as approved canon. Replace only from the Cloud-PASS M10 SAY file on follow-up.

## Slide 6
Small samples use a t multiplier
t*
Depends on confidence level
Depends on degrees of freedom
Larger confidence demand → larger multiplier
MARGIN
margin = t* × standard error
interval = estimate ± margin
Notes: OLI SAY PLACEHOLDER — CLOUD PASS PENDING.
Beat: t multiplier
Do not improvise or treat this scaffold as approved canon. Replace only from the Cloud-PASS M10 SAY file on follow-up.

## Slide 7
Confidence describes a method—not a vote on a claim
95% CONFIDENCE
In repeated sampling, about 95% of intervals built this way capture the true mean
NOT THIS
A 95% chance this calculated interval moves
A 95% chance FOREMAN's story is true
Notes: OLI SAY PLACEHOLDER — CLOUD PASS PENDING.
Beat: confidence level
Do not improvise or treat this scaffold as approved canon. Replace only from the Cloud-PASS M10 SAY file on follow-up.

## Slide 8
IN CLASS — DO THIS NOW
Warm up with six coupons
10 min
1
Open coupons.csv and H10-01.
2
Calculate the mean, sample SD, and SE.
3
Read t* for 95% confidence and df = 5 from the supplied table.
4
Build and interpret the interval on mean yield strength.
The warm-up teaches mechanics; it does not answer the deck question.
Notes: OLI SAY PLACEHOLDER — CLOUD PASS PENDING.
Beat: coupon warm-up
Do not improvise or treat this scaffold as approved canon. Replace only from the Cloud-PASS M10 SAY file on follow-up.

## Slide 9
2
Separate signal from noise
Pair locations and inspect what the test process controlled
Notes: OLI SAY PLACEHOLDER — CLOUD PASS PENDING.
Beat: signal/noise transition
Do not improvise or treat this scaffold as approved canon. Replace only from the Cloud-PASS M10 SAY file on follow-up.

## Slide 10
Pairing asks each location to serve as its own baseline
UNPAIRED QUESTION
How do all 2019 values compare with all 2027 values?
Location differences remain mixed into the spread
PAIRED QUESTION
For each same location, what is 2027 − 2019?
Analyze the eight location changes
Notes: OLI SAY PLACEHOLDER — CLOUD PASS PENDING.
Beat: paired design
Do not improvise or treat this scaffold as approved canon. Replace only from the Cloud-PASS M10 SAY file on follow-up.

## Slide 11
Noise has more than one address
MEASUREMENT
Instrument resolution
Pass-to-pass repeatability
Calibration
PROCESS
Truck load
Lane position
Speed
Temperature handling
SAMPLING
Only eight locations
Change varies by location
SE and interval
Notes: OLI SAY PLACEHOLDER — CLOUD PASS PENDING.
Beat: measurement/process/sampling noise
Do not improvise or treat this scaffold as approved canon. Replace only from the Cloud-PASS M10 SAY file on follow-up.

## Slide 12
IN CLASS — DO THIS NOW
Audit the test before the p-value
8 min
1
Open H10-02 and M10-test-control-check.csv.
2
Verify load, lane position, speed, passes, and temperature handling across years.
3
Compare within-test repeatability SD with each paired change.
4
List one source reduced by design and one uncertainty that remains.
Matched controls reduce alternative explanations; they do not diagnose a mechanism.
Notes: OLI SAY PLACEHOLDER — CLOUD PASS PENDING.
Beat: test-control audit
Do not improvise or treat this scaffold as approved canon. Replace only from the Cloud-PASS M10 SAY file on follow-up.

## Slide 13
IN CLASS — DO THIS NOW
Build the paired 95% interval
12 min
1
Use M10-paired-location-summary.csv and H10-03.
2
Check each 2027 − 2019 change before summarizing.
3
Calculate mean, SD, SE, t* for df = 7, and the 95% interval.
4
Decide whether zero mean change remains plausible at this confidence level.
Commit the interval and a one-sentence claim before the reveal.
Notes: OLI SAY PLACEHOLDER — CLOUD PASS PENDING.
Beat: paired 95% interval
Do not improvise or treat this scaffold as approved canon. Replace only from the Cloud-PASS M10 SAY file on follow-up.

## Slide 14
Significance is not size, certainty, or diagnosis
p-VALUE
Assumes a null model
Asks how unusual this result would be under that model
Does not assign probability to FOREMAN's claim
ENGINEERING CLAIM
Needs magnitude
Needs uncertainty
Needs test controls
May still need a physical mechanism
Notes: OLI SAY PLACEHOLDER — CLOUD PASS PENDING.
Beat: p-value and significance language
Do not improvise or treat this scaffold as approved canon. Replace only from the Cloud-PASS M10 SAY file on follow-up.

## Slide 15
IN CLASS — DO THIS NOW
Raise the confidence level
5 min
1
Keep the same mean, SD, SE, and df.
2
Replace the 95% t multiplier with the 99% multiplier.
3
Rebuild the interval and check whether zero enters.
4
Explain why the two intervals are not contradictory.
Higher confidence requires a wider interval.
Notes: OLI SAY PLACEHOLDER — CLOUD PASS PENDING.
Beat: 99% sensitivity check
Do not improvise or treat this scaffold as approved canon. Replace only from the Cloud-PASS M10 SAY file on follow-up.

## Slide 16
Write Unit 2 Note v2
Claim · check · result · now with an interval
CLAIM
State FOREMAN's 6% and p-value interpretation.
CHECK
Give paired estimate, interval, and noise/control audit.
RESULT
Say how sure—and what the data still cannot prove.
Notes: OLI SAY PLACEHOLDER — CLOUD PASS PENDING.
Beat: Note v2
Do not improvise or treat this scaffold as approved canon. Replace only from the Cloud-PASS M10 SAY file on follow-up.

## Slide 17
Before the gated reveal
HAND IN
H10-03 and H10-06 after committing the paired claim.
ASSIGNED
HW5: audit duplicate timestamps before building the peak-strain interval.
RECORD
Project-hour choice and anything accepted unverified.
BOUNDARY
Keep all Exam 1 scenario details out of M10.
Notes: OLI SAY PLACEHOLDER — CLOUD PASS PENDING.
Beat: HW5 callback and close
Do not improvise or treat this scaffold as approved canon. Replace only from the Cloud-PASS M10 SAY file on follow-up.